## Slide 1: Reinforecement Learning USE TesT case (FOR discussion)
Dec 2021
YeongJu

## Slide 2: Analytics outcome Deployment
Deployment Type | Use Case | Challenge
Quick actions from analytic insight | RC Fan replacement Ball box more frequent replacement | Requires investments (SOP change, sensor installment, machine replacement)
Dashboard / Webapp for informed decisions | Recycle material mix optimization CM – bending and tilting models | Extra efforts to make UI UI maintenance Operators don’t need to follow
Machine Control for optimization | Predictive zone 3 control Air/gas ratio automation (today’s presentation) | Interaction with PLC real time data Working with automation

## Slide 3: CONTENTS
Supervised vs. Reinforcement Learning
RL - Model based vs. Model Free
Perceptron Using Pytorch
Cartpole Problem
Use Test Case – Air/Gas Ratio Automation

## Slide 4: Supervised Learning vs. Reinforcement learning
Reinforcement learning makes sequential decisions to maximize total rewards to come.

## Slide 5: Model based vs. Model Free
Sequential Decision Making
Markov Decision Process (MDP)
Model Based
Model Free
Know transitions
Don’t know transitions
Dynamic
programming
Tree Search
Planning
Reinforcement Learning
Monte
Carlo
Time-Difference
Learning
Solution from sampling
Solution from iterations
(e.g) Chiraq’s inventory solution
DQN (Deep Q Network)

## Slide 6: Pytorch

## Slide 7: Pytorch Coded Perceptron (1/2)
Y = F(x1, x2, x3, x4)
Matrix (5,4)
Matrix (5,1)
Matrix (2,1)
Matrix (4,2)
X1
X2
X3
X4
Neural Network
Y

## Slide 8: Pytorch Coded Perceptron (2/2)
Stacking
Functional
Gradient Descent Optimization
Matrix (2,1)
Matrix (4,2)
Backpropagation
Update weights

## Slide 9: Cartpole Problem
4 states to represent the current observation:
https://youtu.be/XiigTGKZfks
Observe the current states and Find the optimal actions (Left or Right) to keep the pole upright straight.
1 Reward is given if the pole stands upright. (less than 15 degrees)
Trial fails if the pole is more than 15 degrees from vertical
Trial succeeds if movement ticks are more than 500 times

## Slide 10: Open-AI Cartpole Environment
Keep pushing to right side
Keep pushing to left side

## Slide 11: Open-AI Cartpole Environment (Physics)

## Slide 12: Open-AI Cartpole Environment (DQN)
Learning Policy Using DQN

## Slide 13: Deep q Network
Basic Algorithm:
Blue Box – Perfect Q function
Green Box – Current Q function
Red Box - loss function of DQN.
https://towardsdatascience.com/reinforcement-learning-concept-on-cart-pole-with-dqn-799105ca670
“We want to minimize the loss so that there is nothing to learn!”

## Slide 14: Deep q Network
Network We Need
https://towardsdatascience.com/reinforcement-learning-concept-on-cart-pole-with-dqn-799105ca670
https://towardsdatascience.com/welcome-to-deep-reinforcement-learning-part-1-dqn-c3cab4d41b6b

## Slide 15: Deep Q Network
Things We Need to Know before Applying DQN:
Observation States Space : [X1, X2, X3 X4]
Action Space: [0, 1]
Reward Structure: 1 if theta(X3) is less than 15 degree 0 otherwise -> Game Over!
Transition:
  Env.Reset() Initiate a simulation by creating starting states
  Env.Step( action ) Generate ‘next states’, ‘reward’, ‘end flag’ given an action
X1
X2
X3
X4

## Slide 16: Air-Gas Ratio
High air to gas ratio: Too much air and less fuel generates weak heat.
Low air to gas ratio: Too much fuel and less air makes the fuel wasted, because fuel are not turned into heat 100%.
REMELT MELTER

## Slide 17: Air-Gas Ratio
Why Do We Use RL for ‘Air-Gas Ratio’ Problem?
If we were to know the optimal air-gas ratio given situation, then we would be better off doing supervised learning such that Action = F(States)
We simply don’t know the optimal air-gas ratio given states. (Physics engineer probably knows…)
As such, we want to test RL to know if it is working.
For RL to work, we set up a performance reward at the end of cycle.

## Slide 18: Air-Gas Ratio
We must define:
Observation States Space : [X1, X2, X3, X4]
Action Space: [0, 1, 2, 3, 4]
Reward Structure: When the temperature reaches 960, Reward = (1) + (2) (1) Average temp increase / min is greater than 5 degree (speedy temp increase) (2) Average Air/gas ratio (fuel saving)
Transition:
  Env.Reset() Initiate a simulation by randomly selecting starting states
  Env.Step( action ) Generate ‘next states’, ‘reward’, ‘end flag’ given an action
X1: Preheater Temperature
X2: Melter Inner Pressure
X3: Melter Inner Temperature
X4: Cold(Non-Molten) Input (Ton)

## Slide 19: Air-Gas Ratio
Action Space: 5 actions

## Slide 20: Air-Gas Ratio
Transition Function:
F(X1, X2, X3, X4, Action) = Delta (X1, X2, X3)
3 minutes later
X1: Preheater Temperature
X2: Melter Inner Pressure
X3: Melter Inner Temperature
X4: Cold(Non-Molten) Input (Ton)

## Slide 21: Air-Gas Ratio
Melter(Furnace) Environment:
  Env.Reset() Initiate a simulation by randomly selecting starting states
  Env.Step( Action ) - Generate ‘next states’, ‘reward’, ‘end flag’ given an action - Gaussian noise added to the next states
  Random_Action()
    Random action from an action space
Reward is given
when the temperature
reaches above 960
Transition to next states with random noise

## Slide 22: Air-Gas Ratio: Reinforcement Learning
DQN Learning
  Reuse Cartpole scripts with a few parameter tunning
  3,000 simulations
  Reward structure

## Slide 23: Air-Gas Ratio
Performance
Avg Reward = 0.75
Avg Reward = 0.41
Avg Reward = 0.47
RL - Learned Actions (Simulation)
Random Actions (Simulation)
Actual Actions (Real Data)

## Slide 24: Appendix
https://towardsdatascience.com/welcome-to-deep-reinforcement-learning-part-1-dqn-c3cab4d41b6b